Rotational Motion – II

Reading: Chapter 11

Rolling

2 points of view:

(1) Combined rotation and translation

(a) Translation: the center of mass moves with velocity vcm.

(b) Rotation: the wheel rotates about the center of mass.

If the wheel rolls without slipping, s = R(, then

(2) Pure Rotation

Rolling can also be considered as a pure rotation, with angular speed (, about an axis through the contact point. e.g. velocity at the top: vtop = (()(2R) = 2((R) = 2vcm.

Kinetic Energy of Rolling

If we consider the motion as a pure rotation about the contact point,

Using the parallel axis theorem,

Hence , and

The kinetic energy consists of:

- the kinetic energy of the translational motion of the center of mass,

- the kinetic energy of the rotation about the center of mass.

Friction and Rolling

- When the cyclist applies a torque on the wheel intending to make it rotate faster, the bottom of the wheel tends to slide to the left at point P. A frictional force at P, directed to the right, opposes the tendency to slide.

- The frictional force acts on the wheel and produces the acceleration of the bicycle.

Rolling Down a Ramp

The gravitational force tends to make the wheel slide down the ramp. There is a frictional force opposing this sliding, and is thus directed up the ramp.

Using Newton’s second law for translational motion,

(1)

Using Newton’s second law for rotational motion,

(2)

Since a = R(, we obtain from (2): .

Substituting into (1),

Example

11-2 A uniform ball, of mass M = 6.00 kg and radius R, rolls smoothly from rest down a ramp at angle ( = 30.0o.

(a) The ball descends a vertical height h = 1.20 m to reach the bottom of the ramp. What is its final speed?

(b) What are the magnitude and direction of the frictional force on the ball as it rolls down the ramp?

(a) Method 1: Conservation of energy

Other terms: Uf = Ki = 0, Ui = Mgh. Hence

(answer)

Method 2: Newton’s law

Translational motion: 			(1)

Rotational motion: 					(2)

where . Since a = R(, (2): .

(1):

(answer)

(b)

= 8.4 N   (answer)

The Yo-Yo

Using Newton’s second law for translational motion,

(1)

Using Newton’s second law for rotational motion,

(2)

Since a = R0(, we obtain from (2):

.

Substituting into (1),

Angular Momentum

Alternatively,  or .

Newton’s Second Law

The vector sum of all the torques acting on a particle is equal to the time rate of change of the angular momentum of that particle.

Proof

Differentiating with respect to time,

because the angle between  and itself is zero.

Using Newton’s law,  Hence

Since , we arrive at

The Angular Momentum of a System of Particles

Total angular momentum for n particles:

Newtons’ law for angular motion:

includes torques acting on all the n particles. Both internal torques and external torques are considered.

Using Newton’s law of action and reaction, the internal forces cancel in pairs. Hence

The Angular Momentum of a Rigid Body

For the ith particle, angular momentum:

The component of angular momentum parallel to the rotation axis (the z component):

The total angular momentum for the rotating body

This reduces to

Conservation of Angular Momentum

If no external torque acts on the system,

Law of conservation of angular momentum.

Examples

1. The spinning volunteer: When the student pulls in the dumbbells, the rotational inertia I decreases. Since , the angular velocity increases.

2. The springboard diver: When the diver is in the tuck position, the rotational inertia decreases, and the angular velocity increases.

When the diver is in the layout position, the rotational inertia increases, and the angular velocity decreases.

3. Long jump: When an athlete takes off, her angular momentum gives her a forward rotation around a horizontal axis.

In the air, the jumper shifts the angular momentum to her arms by rotating them in a windmill fashion. Then the body carries little angular momentum, keeping her body upright. She can then land with her legs extended forward.

4. Tour jeté: The dancer/gymnast leaps with one leg perpendicular to the body. In the air, the outstretched leg is brought down and the other leg is brought up, with both ending up at an angle ( to the body. The rotational inertia decreases and the angular speed increases.

On landing, a leg is again outstretched and the rotation seems to vanish.

See Youtube “Chen Helps China Sweep”, “Irving Saladino” and “tour jete”.

See demonstration “Bicycle wheel gyroscope” and “swinging Atwood machine”.

Examples

11-7 A student sits on a stool that can rotate freely about a vertical axis. The student, initially at rest, is holding a bicycle wheel whose rim is loaded with lead and whose rotational inertia I about its central axis is 1.2 kg m2. The wheel is rotating at an angular speed (wh of 3.9 rev/s; as seen from overhead, the rotation is counterclockwise. The axis of the wheel is vertical, and the angular momentum Lwh of the wheel points vertically upward. The student now inverts the wheel; as a result, the student and stool rotate about the stool axis. The rotational inertia Ib of the student + stool + wheel system about the stool axis is 6.8 kg m2. With what angular speed (b and in what direction does the composite body rotate after the inversion of the wheel?

Using the conservation of angular momentum,

(ans)

11-8 A cockroach with mass m rides on a disk of mass 6m and radius R. The disk rotates like a merry-go-round around its central axis at angular speed (i = 1.5 rad s(1. The cockroach is initially at radius r = 0.8R, but then it crawls out to the rim of the disk. Treat the cockroach as a particle. What then is the angular speed?

Using the conservation of angular momentum,

Rotational inertia:

The disk:

The cockroach:  and

Therefore,

(ans)

Precession of a Gyroscope

Torque due to the gravitational force

Angular momentum

For a rapidly spinning gyroscope, the magnitude of  is not affected by the precession,

Using Newton’s second law for rotation,

where  is the precession rate

Example Rolling of a Hexagonal Prism (1998 IPhO)

Consider a long, solid, rigid, regular hexagonal prism like a common type of pencil. The mass of the prism is M and it is uniformly distributed. The length of each side of the cross-sectional hexagon is a. The moment of inertia I of the hexagonal prism about its central axis is I = 5Ma2/12.

a) The prism is initially at rest with its axis horizontal on an inclined plane which makes a small angle ( with the horizontal. Assume that the surfaces of the prism are slightly concave so that the prism only touches the plane at its edges. The effect of this concavity on the moment of inertia can be ignored. The prism is now displaced from rest and starts an uneven rolling down the plane. Assume that friction prevents any sliding and that the prism does not lose contact with the plane. The angular velocity just before a given edge hits the plane is (i while (f is the angular velocity immediately after the impact. Show that (f = s(i and find the value of s.

b) The kinetic energy of the prism just before and after impact is Ki and Kf. Show that Kf = rKi and find r.

c) For the next impact to occur, Ki must exceed a minimum value Ki,min which may be written in the form Ki,min = (Mga. Find ( in terms of ( and r.

d) If the condition of part (c) is satisfied, the kinetic energy Ki will approach a fixed value Ki,0 as the prism rolls down the incline. Show that Ki,0 can be written as Ki,0 = (Mga and find (.

e) Calculate the minimum slope angle (0 for which the uneven rolling, once started, will continue indefinitely.

a) Angular momentum about edge E before the impact

Angular momentum about edge E after the impact

Using the conservation of angular momentum, Li = Lf

(      (

b)

(      (

c) After the impact, the center of mass of the prism raises to its highest position by turning through an angle 90o ( (( + 60o) = 30o ( (. Hence

(

d) At the next impact, the center of mass lowers by a height of asin(. Change in the kinetic energy

Kinetic energy immediately before the next impact

When the kinetic energy approaches Ki,0,

(      (

e) For the rolling to continue indefinitely,

(

where A = r/(1 ( r) = 121/168 and

( u ( 35.36o.

( ( + u ( 41.94o.   (   (0 ( 6.58o.

# Text boxes

blurred

clear

R

R0

(

Pi

Pf

30o

E