Longitudinal Waves

Reading: Chapter 17, Sections 17-7 to 17-10

Sources of Musical Sound

Pipe

Closed end: node

Open end: antinode

Standing wave pattern:

Fundamental or first harmonic: 2 nodes at the ends, 1 antinode in the middle

Resonant frequency:

In general, for harmonic number n,

for n = 1, 2, 3,

Resonant frequency:

for n = 1, 2, 3,

For pipes with only one open end,

In general,

for n = 1, 3, 5, …

Resonant frequencies:

for n = 1, 3, 5, …

In general, when a musical instrument produces a tone, the fundamental as well as higher harmonics are generated simultaneously. This gives rise to the different waveforms generated by different instruments.

Hence different instruments have different sounds.

Example

17-6 Weak background noises from a room set up the fundamental standing wave in a cardboard tube of length L = 67.0 cm with two open ends. Assume that the speed of sound in the air within the tube is 343 ms-1.

(a) What frequency do you hear from the tube?

(b) If you jam your ear against one end of the tube, what fundamental frequency do you hear from the tube?

(a) Two open ends,

(ans)

(b) One fixed end and one open end,

(ans)

Beats

Consider two sound waves with slightly different frequencies:

and

Resultant displacement:

Using the trigonometric identity

we obtain

Conclusion:

where

and

Since (1 and (2 are nearly equal, ( >> (’.

Hence the resultant displacement consists of an oscillation with angular frequency ( and a slowly changing amplitude with angular frequency (’.

The amplitude 2smcos(’t is maximum when cos(’t = (1, i.e. 2 times in each repetition of the cosine function.

Hence the beat frequency is:

Musicians use the beat phenomenon in tuning their instruments.

See Animation “Beats”

The Doppler Effect

See Youtube “Fire Engine siren demonstrates the Doppler Effect” and “Example of Doppler Shift using car horn”

Detector Moving; Source Stationary

In time t,

the wavefronts move a distance vt,

the detector moves a distance vDt,

the range of waves intercepted by the detector = vt+vDt,

the number of wavefronts intercepted by the detector = (vt+vDt)/(.

The frequency observed by the detector:

Since (=v/f,

Similarly, if the detector moves away from the source,

Summarizing,

Source Moving; Detector Stationary

In a period T,

the distance moved by the wavefront W1 = vT,

the distance moved by the source = vST,

the distance between the wavefronts W1 and W2

= vT( vST.

The frequency observed by the detector:

If the source moves away from the detector,

Summarizing,

General Doppler Effect Equation

When both the source and detector are moving,

vS = 0 reduces to the equation for stationary source.

vD = 0 reduces to the equation for stationary detector.

Example

17-8 Bats navigate and search out prey by emitting, and then detecting reflections of, ultrasonic waves, which are sound waves with frequencies greater than what can be heard by a human. Suppose a bat emits ultrasound at frequency fbe = 82.52 kHz while flying with velocity vb = 9.00 ms(1. It chases a moth that flies with velocity vm = 8.00 ms(1.

(a) What frequency fmd does the moth detect?

(b) What frequency fbd does the bat detect in the returning echo from the moth?

(a) Detection by moth:

(ans)

(b) Detection of echo by bat:

(ans)

Supersonic Speeds; Shock Waves

When v approaches vS, f’ becomes infinity since .

When v exceeds vS, the Doppler effect equation does not apply. All wavefronts bunch along a V-shaped envelope. This is called the Mach cone. A shock wave is produced.

Note that the envelope touches the circular wavefronts. Therefore the radius ending at the tangent point is normal to the Mach cone.

Mach cone angle:

vS/v is called the Mach number.

When is the Boom Heard?

The sonic boom detected by a ground observer was generated by a supersonic jet before it flies overhead.

However, when sonic boom arrives at the ground observer, the supersonic jet has flown ahead (located at the tip of the Mach cone).

Example

The speed of sound is 340 ms-1. A plane flies horizontally at an altitude of 10,000 m and a speed of 400 ms-1. When an observer on the ground hears the sonic boom, what is the horizontal distance from the point on its path directly above the observer to the plane?

From the figure,

# Text boxes

L = (/2

L = (/4

fbe

fm

fm

fbd

vb

vm

See Youtube “Sonic Boom”

x

h

(

10,000 m

340t

(

400t

x